## Slide 1
MACHINE LEARNING | 25SC2107E | ACADEMIC YEAR 2026-27
Multi-Task CNN-Transformer for Joint OTFS Channel Estimation and Doppler-Sensing Prediction
Srikar Prathap
2520040006
Dakshesh Kumar
2520040060
Dhanush Karthikeya
2520040032
Under the guidance of Mr. N Lava Prasad, Assistant Professor, Department of ECE
Notes: Introduce the project title, team and guide.

## Slide 2
INTRODUCTION
Why High-Mobility Wireless Needs Smarter Receivers
Joint OTFS Channel Estimation & Doppler Prediction
2
Orthogonal Time Frequency Space (OTFS) is a modulation technique built for high-mobility links. Vehicle motion, multipath propagation and Doppler shifts make the channel vary quickly, so the receiver must know the channel and the Doppler shift accurately.
Our idea
One shared CNN-Transformer learns channel features and solves both tasks together: channel estimation and Doppler prediction.
Autonomous vehicles
Reliable links under rapidly changing speeds.
Drones and UAVs
Communication during high-speed flight.
High-speed trains
Estimation under large Doppler shifts.
5G and 6G networks
ML-based signal processing for future systems.
Notes: OTFS works in the delay-Doppler domain; fast-moving users make the channel change rapidly.

## Slide 3
PROBLEM STATEMENT
What We Set Out to Solve
Joint OTFS Channel Estimation & Doppler Prediction
3
PROBLEM
Develop a machine-learning approach that jointly performs channel estimation and Doppler-sensing prediction from OTFS received-signal data.
Proposed solution
A shared CNN-Transformer with two output heads.
1
Rapid channel variation
User mobility and multipath make the channel change quickly.
2
Noise and Doppler effects
Both make accurate channel estimation difficult.
3
Separate processing is costly
Doing the two tasks apart needs extra processing.
4
Need for shared learning
A joint model can reuse features across both tasks.

## Slide 4
PROPOSED METHODOLOGY
A Joint CNN-Transformer Approach
Joint OTFS Channel Estimation & Doppler Prediction
4
A CNN extracts local features from the delay-Doppler input; a Transformer encoder then learns how different delay-Doppler bins relate; one shared representation feeds both tasks.
1
CNN feature extraction
Finds local patterns in the received OTFS signal.
2
Transformer encoder
Uses attention to learn long-range links between delay-Doppler bins.
3
Multi-task learning
Shares one feature representation across both tasks.
Joint prediction: channel response estimate plus Doppler-related outputs from the same backbone.

## Slide 5
ALGORITHM
Model Architecture and Training Pipeline
Joint OTFS Channel Estimation & Doppler Prediction
5
STAGE 1
OTFS input
Delay-Doppler grid with real and imaginary parts
›
STAGE 2
CNN encoder
Convolutional layers extract local features
›
STAGE 3
Transformer encoder
Feature tokens learn long-range dependencies
›
STAGE 4
Shared features
One representation for both tasks
›
Channel head
Doppler head
Channel head
Estimates the channel response on the delay-Doppler grid.
Doppler head
Predicts normalized Doppler and its Low / High class.
Training
Joint optimisation with a combined loss over both tasks.

## Slide 6
IMPLEMENTATION
Workflow and Simulation Setup
Joint OTFS Channel Estimation & Doppler Prediction
6
1
Generate synthetic OTFS channels with multipath and Doppler
2
Add AWGN noise and prepare the delay-Doppler input
3
Extract local features with CNN layers
4
Tokenise features for the Transformer encoder
5
Train the joint estimation and prediction model
6
Evaluate with estimation and prediction metrics
Parameter | Specification
Representation | OTFS-like delay-Doppler grid
Input | Two channels (real, imaginary)
Channel model | Synthetic multipath
Noise | AWGN
Dataset | 5,800 synthetic samples
Data split | 4000 train / 800 val / 1000 test
Tools: Python, Google Colab, TensorFlow/Keras, NumPy, Matplotlib, Scikit-learn
Metrics: MSE, NMSE (channel); MAE, RMSE, accuracy, ROC-AUC (Doppler)

## Slide 7
RESULTS 1 / 5
Training and Validation Loss
Joint OTFS Channel Estimation & Doppler Prediction
7
0.08
Final train loss
0.14
Final val loss
Fast drop in the first 5 epochs (train 0.95, val 0.69 at start)
Slow plateau from epoch 6 to 15, then a second drop
One brief validation spike near epoch 21, recovered by epoch 22
Train-val gap stays small (0.08 vs 0.14): stable learning, mild overfitting
Notes: Combined loss over 25 epochs (0-24).

## Slide 8
RESULTS 2 / 5
Doppler Prediction: True vs Predicted
Joint OTFS Channel Estimation & Doppler Prediction
8
16
Doppler levels, -1 to 0.875
Mid-range
Most accurate region
Predictions follow the ideal diagonal across the full range
Points near -0.5 to -0.25 and 0.25 to 0.6 sit closest to the line
Extremes are pulled toward the centre: true 0.875 is often predicted at 0.3 to 0.6
A few outliers remain, e.g. true 0.75 predicted near -0.7

## Slide 9
RESULTS 3 / 5
Low vs High Doppler Classification
Joint OTFS Channel Estimation & Doppler Prediction
9
68.2%
Accuracy (307 / 450)
82.2%
Precision, High class
58.0%
Recall, High class
82.4%
Recall, Low class
Only 33 of 188 Low samples are wrongly called High
110 of 262 High samples are missed (called Low)
F1 score is about 0.68 for both classes
The model leans toward predicting Low

## Slide 10
RESULTS 4 / 5
ROC Curve for Doppler Classification
Joint OTFS Channel Estimation & Doppler Prediction
10
AUC = 0.781
Well above the 0.5 of random guessing
About 0.5 true positive rate at only 0.1 false positive rate
About 0.65 TPR at 0.2 FPR and 0.78 at 0.4 FPR
Curve stays above the diagonal everywhere
Moving the decision threshold can trade precision for High-class recall

## Slide 11
RESULTS 5 / 5
Channel Estimation on the Delay-Doppler Grid
Joint OTFS Channel Estimation & Doppler Prediction
11
Paths located
The four dominant paths (about delay, Doppler = 0,0; 2,4; 13,13; 15,11) appear in the estimate.
Amplitudes close
Strongest path about 12.8 true vs 11.7 estimated; error is mostly under 1 elsewhere.
Largest error
Peak error about 2.4 at the weak path near (13,13), partly shifted to delay 14.
Notes: Left: true channel; middle: estimated; right: absolute error.

## Slide 12
RESULTS SUMMARY
Key Findings at a Glance
Joint OTFS Channel Estimation & Doppler Prediction
12
Task | Evidence | Outcome
Training | Loss 0.95 to 0.08 (train), 0.69 to 0.14 (val) | Stable convergence over 25 epochs
Doppler regression | True vs predicted scatter, 16 levels | Follows diagonal; weaker at extremes
Doppler classification | Accuracy 68.2%, F1 about 0.68 | High precision (82.2%), lower High recall (58.0%)
Ranking quality | ROC AUC 0.781 | Clearly better than chance
Channel estimation | 16 x 16 delay-Doppler map | Main paths recovered; max error about 2.4

## Slide 13
CONCLUSION
Conclusion and Future Work
Joint OTFS Channel Estimation & Doppler Prediction
13
What we achieved
A joint CNN-Transformer for channel estimation and Doppler prediction
Stable training with validation loss near 0.14
Doppler classification AUC of 0.781
Main channel paths recovered on the delay-Doppler grid
Future work
Improve High-Doppler recall (class weights, threshold tuning)
Compare against baseline estimators across SNR levels
Test under more channel conditions and noise levels
Reduce the train-validation gap with regularisation

## Slide 14
Thank you
Questions?
Srikar Prathap | Dakshesh Kumar | Dhanush Karthikeya